## Slide 1: Weekly report
Mar 14 2024

## Slide 2
jtag and debug interface
1. JTAG: jtag interface, tap controller, some dmi register
2. CDC: synchronized jtag signal and DM signal
3. Debug module

## Slide 3
jtag architecture

## Slide 4
jtag architecture
//register dtmcs:
input [3:0]dtmcs_version_i
input [5:0]dtmcs_abits_i
input [1:0]dtmcs_dmistat_i
input [2:0]dtmcs_idle_i
output dtmcs_dmireset_o
output dtmcs_dmihardreset_o
//jtag interface:
input jtag_trstn_i
input jtag_tck_i
input jtag_tms_i
input jtag_tdi_i
output jtag_tdo_o
output jtag_tdo_enable_o
//register dmi:
input: [2:0]dmi_op_i
input: [31:0]dmi_rdata_i
input: dmi_rdata_valid_i
input: dmi_ack_i
output: dmi_we_o
output: [31:0]dmi_addr_o
output: [31:0]dmi_wdata_o
output: dmi_req_o

## Slide 5
jtag - FSM

## Slide 6
State | select_ir | select_dr | captuer_ir | shift_ir | update_ir | capture_dr | shift_dr | update_dr | tdo_enable
TEST_LOGIC_RESET | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
RUN_TEST_IDLE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SELECT_DR_SCAN | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SELECT_IR_SCAN | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
CAPTURE_IR | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
SHIFT_IR | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
EXIT1_IR | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
PAUSE_IR | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
EXIT2_IR | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
UPDATE_IR | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
CAPTURE_DR | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
SHIFT_DR | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
EXIT1_DR | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
PAUSE_DR | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
EXIT2_DR | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
UPDATE_DR | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
jtag - FSM

## Slide 7
jtag - 1bit shift register

## Slide 8
jtag - 1bit shift register w/o FFstore

## Slide 9
jtag - IR

## Slide 10
jtag - IR
1. capture default value (5'b0_0001)
2. shift 1st tdi
3. shift 2nd tdi
4. shift 3rd tdi
5. shift 4th tdi
6. shift 5th tdi
7. store shift data
ST0: TEST_LOGIC_RESET
ST1: RUN_TEST_IDLE
ST2: SELECT_DR_SCAN
ST3: SELECT_IR_SCAN
IR - decoder:
BYPASS: 5'b1_1111 or 5'b0_0000 -> select_bypass
IDCODE: 5'b0_0001 -> select_idcode
DTMCS: 5'b1_0000 -> select_dtmcs
DMI: 5'b1_0001 -> select_dmi

## Slide 11
jtag - DR

## Slide 12
jtag - DR - BYPASS
capture_bypass = select_bypass & capture_dr
shift_bypass = select_bypass & shift_dr

## Slide 13
jtag - DR - IDCODE
capture_idcode = select_idcode & capture_dr
shift_idcode = select_idcode & shift_dr

## Slide 14
jtag - DR - DTMCS

## Slide 15
jtag - DR - DTMCS
capture_dtmcs = select_dtmcs & capture_dr
shift_dtmcs = select_dtmcs & shift_dr
dtmcs_reg_in[31:0] = { 14'h0, dtmcs_dmihardreset_o,
dtmcs_dmireset_o,
1'h0,
dtmcs_idle_i,
dtmcs_dmistat_i,
dtmcs_abits_i,
dtmcs_version_i}

## Slide 16
jtag - DR - DMI

## Slide 17
jtag - DR - DMI
capture_dmi = select_dmi & capture_dr
shift_dmi = select_dmi & shift_dr

## Slide 18
jtag - DR - DMI
get dmi_rdata_i @posedge dmi_rddata_valid_i if opcode = 2'b01 (read)
update dmi_wdata_o @UPDATE_DR if opcode = 2'b10 (write)

## Slide 19
jtag - dmi handshake
req_set = update_dmi (1cycle) & dmi_ack_i -> request new read/write data if dmi bus is free
req_clr = @posedge dmi_ack_i -> acknowledge receipt of the request
update dmi_we_o @UPDATE_DR if valid opcode (2'b01 -> read ; 2'b10 -> write)

## Slide 20
jtag - tdo
tdo is driven by negedge of tck

## Slide 21
Task | Status | Note
model FEC | done | 
study JTAG |  | 
investigate debug module |  | 
Status